## Slide 1: Example Setup
Area A
Area B
Area C
EDAM Participating Capacity:
1,000 MW
EDAM Participating Capacity:
1,000 MW
EDAM Participating Capacity:
1,000 MW

## Slide 2: RSE Requirements
Area A
Area B
Area C
Avail. Capacity | 1,000 MW |  | 1,000 MW |  | 1,000 MW | 3,000 MW
Demand Forecast | 800 MW |  | 730 MW |  | 795 MW | 2,325 MW
Reserve | 100 MW |  | 100 MW |  | 100 MW | 300 MW
Uncertainty | 100 MW |  | 100 MW |  | 100 MW | 300 MW
Remaining | 0 MW |  | 70 MW |  | 5 MW | 75 MW
Footprint Summary

## Slide 3: IFM Solution (IRU procurement distributed)
Area A
Area B
Area C
Avail. Capacity | 1,000 MW |  | 1,000 MW |  | 1,000 MW | 3,000 MW
Demand Forecast | 800 MW |  | 730 MW |  | 795 MW | 2,325 MW
Reserve | 100 MW |  | 100 MW |  | 100 MW | 300 MW
Uncertainty | 100 MW |  | 100 MW |  | 100 MW | 300 MW
IRU Awards | 0 MW |  | 100 MW |  | 200 MW | 300 MW
Energy Transfer | 100 MW |  | 0 MW |  | 100 MW | 0 MW
IRU Transfer | 100 MW |  | 0 MW |  | 100 MW | 0 MW
Footprint Summary
Energy
100 MW
100 MW
100 MW
100 MW
IRU
Energy
IRU

## Slide 4: IFM Solution (IRU procurement concentrated in A)
Area A
Area B
Area C
Avail. Capacity | 1,300 MW |  | 1,000 MW |  | 1,000 MW | 3,000 MW
Demand Forecast | 800 MW |  | 730 MW |  | 795 MW | 2,325 MW
Reserve | 100 MW |  | 100 MW |  | 100 MW | 300 MW
Uncertainty | 100 MW |  | 100 MW |  | 100 MW | 300 MW
IRU Awards | 300 MW |  | 0 MW |  | 0 MW | 300 MW
Energy Net Transfer | 100 MW |  | 0 MW |  | 100 MW | 0 MW
IRU Net Transfer | 200 MW |  | 100 MW |  | 100 MW | 0 MW
Footprint Summary
Energy
100 MW
100 MW
Energy
100 MW
200 MW
IRU
IRU

## Slide 5: Questions and Answers
What is the scheduling priority of a transfer?
  No priority; it is scheduled economically and it is re-optimized in WEIM
What is the firmness of a transfer?
  The underlying transmission capacity is highly reliable; the transfer schedule is economic (forward financial position) and it is re-optimized in WEIM
Does a transfer increase reserve requirements in EDAM?
  No; there is no need to explicitly procure reserves for it, the market does it
    In the example, 100MW of IRU awards in BAA C can be dispatched in WEIM to back off the day-ahead energy transfer to meet materialized uncertainty in BAA A
What if there is a generator forced outage in BAA A?
  Contingency reserve is dispatched in BAA A to substitute for lost supply
What if there is an outage on an intertie that supports a transfer
  WEIM will back of the energy transfer by re-dispatching resource schedules and awards
    In the example, 100MW of IRU awards in BAA C will be dispatched to make up for the input transfer loss and 100 MW energy supply schedules in BAA A will be converted to FRU awards
    Depending where the IRU is being carried other dispatch results can occur but so long as the IRU is feasibly procured, it should be able to meet collective realized uncertainty.

## Slide 6: Emergency Conditions
What if a contingency occurs beyond the MSSC?
  All contingency reserve is dispatched, yet more is needed
  Flexible Ramp Up can be dispatched
    What if uncertainty also materializes depleting all flexible ramp up awards
What if uncertainty materializes beyond the 95th percentile in every BAA in the market footprint?
  All flexible ramp up awards and all energy bids are dispatched, but need more
Market cannot calculate a feasible solution (power balance relaxation)
  Operator action needed out of the market
    Conditional supply or demand response dispatch
    Emergency assistance from other BAAs
    Manual commitment and dispatch of capacity not in the market
    Interruptible demand options
    Pro rata export cut and load management